## Slide 2
Detection of thermal neutrons and its applications
Luis Ricardo Beltran, Deywis Moreno
Bogotá, Colombia
2026

## Slide 3
Introduction

## Slide 4
Neutron interaction
Main difficulties of detection:
Neutrons are electrically neutral.
They do not ionize matter directly.
Detection relies on interaction with a converter material to produce detectable charged particles

## Slide 5
Neutron interaction
Cross-section of the boron-10 and boron-11 as a function of neutron energy. Source: Reproduced
From: [1]
Neutron category | Energy
Thermal Neutron | <0.025eV
Epithermal Neutron | >0.025eV <1eV
Fast Neutron | >1eV
Neutron category by energy

## Slide 6
Theoretical framework
Capture of neutron for

## Slide 7
Applications

## Slide 8
Applications – Neutron Imaging
Source: https://www.iaea.org/bulletin/advances-in-neutron-imaging-create-opportunities-for-low-power-research-reactors
The neutron imaging system at the Czech Technical University in Prague (CTU) revealed an axis mundi (a symbol of the connection between the physical and spiritual worlds) inside a Tibetan Bon statue of Chamma. (Photos: L. Sklenka/CTU)

## Slide 9
Source: https://taelifesciences.com/developing-targeted-drugs-for-boron-neutron-capture-therapy-to-treat-refractory-cancers/
Applications - BNCT For Cancer

## Slide 10
Source: https://www.apnga.com/gauge-basics/
Applications - Engineering
Nuclear Densimeter

## Slide 11
Setup

## Slide 12
Setup
Boron-doped graphene film
SP5600AN Educational Kit - Premium Version
Lab Nanomateriales of UniAndes
Prof. Yenny Hernandez

## Slide 13
Methodology

## Slide 14
System Design
Am-Be Source
Generate Neutrons of mean energy of 4.5MeV and Gammas of 4.4MeV
Paraffine moderator
Thermalization of fast neutrons to 0.025ev
Boron-Graphene Film
Capture of thermal neutrons and generate alpha particles, Li7 ions and gammas (0,48MeV)
Scintillator Crystal
The gammas deposited their energy and generate optical photons
SiPM
Generate an electric signal for one optical photon
Fast Neutrons
Thermal Neutrons
Optical
Photons

## Slide 15
Simulation

## Slide 16
Geant4 Simulation
Geant4 (11.4.0): Monte Carlo simulation of neutron transport, geometry design and interactions.
ROOT (6.37.1): Analysis of energy spectra and particle distributions.
Uproot (5.6.6): Python library for automated extraction of ROOT data for batch processing.

## Slide 17
Thermalization
Geometry:
Lead (x=20cm, y=20cm z=4cm)
Paraffine (x,y,z variables)
Detector
Primary Generator Action:
Neutrons and gamma source:
AmBe ISO 8529-1
Physics:
QGSP_BERT_HP

## Slide 18
Thermalization – AmBe Source
  Isotropic
  range 0-11 MeV
  mean ~4.5 MeV
  60% of times generate one gamma of 4.4 Mev

## Slide 19
Thermalization – Thickness, Height and Width
Events for simulation:
100,000 events
Total simulations:
  8,000
Geometry Paraffin
0cm< x <20cm
0cm< y <20cm
0cm< z <20cm
Step = 1cm

## Slide 20
Thermalization – Thickness, Height and Width
Geometry Select:
  Height=12cm
  Width=12 cm
  Thickness= 8cm

## Slide 21
Thermalization - Energy spectrum and particles for (12x12x8) Paraffin
Particles | Counts | % of 1,000,000 events
Fast Neutron | 1495 | 0.15%
Thermal Neutron | 446 | 0.04%
Gamma | 1014 | 0.10%
Electron | 14 | 0.001%
Positron | 1 | 0.0001%
Proton | 1 | 0.0001%
Total | 2971 | 0.29%

## Slide 22
Neutron capture
Geometry:
Kapton (r=1.4cm, thickness=120um)
Film Graphene-B10 (r=1.3cm, thickness=Variable um)
% Of boron:
Variable
Primary Generator Action:
Particles in detector of Phase 1 after thermalization
Physics:
QGSP_BERT_HP

## Slide 23
% Capture vs %Boron

## Slide 24
% Particles in detector vs %Boron

## Slide 25
% Capture vs Graphene thickness

## Slide 26
% Particles in detector vs Graphene thickness

## Slide 27
Neutron capture results – Particles created
Events for simulation:
1’000.000 events
(a)
(b)
(c)

## Slide 28
Scintillator and SiPM
Geometry:
Scintillator crystal BGO (6x6x15)mm3
SiPM (6x6)mm2
Physics:
FTFP_BERT + G4OpticalPhysics
Primary Generator Action:
Particles in detector of Phase 2 after capture

## Slide 29
Scintillator and SiPM calibration
Simulation Cs137 (gamma-661.7Kev)
Experimental data Cs137 (gamma-661.7Kev)

## Slide 30
SiPM Response in PE

## Slide 31
SiPM Response in PE

## Slide 32
Conclusions
A three-step Monte Carlo model was successfully implemented to simulate the full detection chain of thermal neutrons.
The optimal geometry for thermalization was found to be a Paraffin block of 12 × 12 × 8 cm.
The boron-doped graphene film successfully produced the expected reaction products (α and 7Li). Additionally, the simulation revealed the presence of soft photons, which must be accounted for in the signal analysis.
The BGO Crystal generated a signal that allowed the background to be differentiated.

## Slide 33
Future Work
Experimental Validation: Test the detection in laboratory conditions using the neutron source facilities at UPTC.
Simulate alternative scintillator materials (LYSO, NaI(Tl), CsI, Plastic) and compare their SiPM response in terms of light yield and energy resolution.

## Slide 34
Acknowledgments
I would like to express my gratitude to:
The Nanomaterials Research Group at Universidad de los Andes for their collaboration on the material preparation and characterization on Boron doped graphene in particular Prof. Yenny Hernandez.
The High Energy Physics Group at Universidad de los Andes in special Prof. Carlos Avila.
The High Energy Physics Group at Universidad Antonio Nariño (UAN) for their academic support and resources.

## Slide 35
References
C. Paganelli, D. Broggio, A. Zanini. Boron-10 and Boron-11 neutron cross-sections for BNCT: New data and evaluation. Applied Radiation and Isotopes, 147 (2019) 38–45.
S. Agostinelli et al. GEANT4 – A simulation toolkit. Nucl. Instrum. Meth. A 506 (2003).
J. Allison et al. Recent developments in Geant4. Nucl. Instrum. Meth. A 835 (2016).
ROOT Data Analysis Framework. CERN. https://root.cern
M. S. Dewji et al. Neutron detection principles and applications. Oak Ridge National Laboratory (2013).
David Cepeda. Simulación de la interacción neutrónica en películas de grafeno dopadas con boro usando geant4. Universidad Antonio Nariño, 2025.

## Slide 37
Backup

## Slide 38
Backup

## Slide 39
Backup

## Slide 40
SP5600AN – Educational Kit – Premium Version
Backup

## Slide 41
Backup